| Project Network # |  | Drawing # |  |
| --- | --- | --- | --- |
| Project Name |  |
| Location |  |
| Project Type | Network Managed Project | Customer Managed Project |
|  | Residential | Residential |
|  | Industrial/Commercial | Industrial/Commercial |
|  | Public Lighting | Public Lighting |
| PROJECT SCOPE (Brief description) |
| Network Project Manager |  |
| Location. |  | Phone No |  | Email |  |
| Customer Project Manager |  |
| Location. |  | Phone No |  | Email |  |
| Electrical Constructor |  |
| Contact |  | Phone No |  | Email |  |
| Civil Contractor |  |
| VEDN No. |  | Phone No |  | Email |  |
| Worksite Auditor/s |  |
| VEDN No. |  | Phone No |  | Email |  |
| Network Auditor |  |
| VEDN No. |  | Phone No |  | Email |  |
| Cable Detailer |  |
|  |  | Phone No |  | Email |  |
| Network Auditor |  |
| Phone No. |  | Mobile No |  | Email |  |
| ASSESSMENT DETAILS |
| Initiator |  | Audit Date |  |
| Position |  | Auditor |  |
| Company |  | Company |  |

| INSPECTION ITEM GUIDELINES | Comp y/n/na | Date | Initials | Comments |
| --- | --- | --- | --- | --- |
| DESIGN SPECIFICATION |
| Approved construction drawing provided (current) |  |  |  |  |
| SITE REFERENCES |
| Lot title boundaries pegged |  |  |  |  |
| Kerb & channel installation complete |  |  |  |  |
| Final surface levels can be determined |  |  |  |  |
| TRENCH |
| WIDTH - To design specification eg. shared use |  |  |  |  |
| DEPTH - Compliant with plan and final surface level |  |  |  |  |
| OFFSET - Alignment correct |  |  |  |  |
| DEVIATION - No unapproved route deviations |  |  |  |  |
| JOINT HOLES – correct size |  |  |  |  |
| BEDDING SAND |
| Correct depth when compacted (min 50mm) |  |  |  |  |
| Correct grade/type |  |  |  |  |
| Free of rocks, sharp or foreign objects |  |  |  |  |
| SERVICE PITS |
| Location – correct boundaries |  |  |  |  |
| Entry conduits installed (75mm +/- 25 mm into pit) |  |  |  |  |
| Body not distorted, lid fitted & operational |  |  |  |  |
| CONDUITS |
| Correct size and category |  |  |  |  |
| DEPTH - Compliant with plan and final surface level |  |  |  |  |
| Road crossing – Telco separation (100mm LV & 300mm HV) incl. tape |  |  |  |  |
| Separation to other utilities (as specified by Network Owner) |  |  |  |  |
| Road crossing – extension past BOK & stormwater |  |  |  |  |
| Spare/future conduits capped or sealed |  |  |  |  |
| Warning tape installed (300mm +/- 50mm from final ground level) |  |  |  |  |
| AS BUILT DETAILS |
| Assets details recorded prior to cover/backfill |  |  |  |  |
| Supporting digital photographs recorded/attached |  |  |  |  |
| Provide Name and Company responsible (Recognised Cable Detailer) |  |
| SUBSTATION RESERVE (Where specified) |
| Free of all other authorities’ underground assets |  |  |  |  |
| Site flat and level |  |  |  |  |
| Substation site dimensions as per Technical Standard |  |  |  |  |
| If specified: retaining wall, batter & drainage installed |  |  |  |  |
| Foundation culvert installed and level as per Technical Standard |  |  |  |  |
| Foundation located correctly within substation site |  |  |  |  |
| NOTES (Attach extra sheets as required) |
| Note: All non-compliances must be rectified or variations approved by Network Owner Project Manager prior to submission of the completed Civil and Electrical Open Trench Audit Report. |
| DECLARATION |
| The above project -: complies does not comply with all relevant Network Technical Standards and approved drawings at the time of audit inspection. (Tick as applicable) |
| Approved Worksite Civil or Electrical or Network Auditor |
| Audited by |  | VEDN No. |  |
| Signature |  | Date |  |