Note: The following information is to be used as a guideline only. The Host Network Project specific standards/requirements and approved drawings will take precedence over the general information provided in this document.

- Prior to any excavation you are required to confirm minimum separation distances required by the asset owner.

- The utility may provide an exemption but this must be in writing

- This table is based on trenches less than 1500mm wide

| Electricity Distribution underground cables | Telco Asset | Gas Transmission | Gas Asset < 50mm | Gas Asset > 50mm | Water Main < 300mm | Water Main > 300mm |
| --- | --- | --- | --- | --- | --- | --- |
|  | Horizontal Separation | Vertical Separation | Horizontal Separation | Vertical Separation | Horizontal Separation | Vertical Separation | Horizontal Separation | Vertical Separation | Horizontal Separation | Vertical Separation | Horizontal Separation | Vertical Separation |
| HV | 300 | 300 | 1000 | 1000 | 300 | 150 | 500 | 150 | 500 | 300 | 500 | 300 |
| LV | 100 | 100 | 1000 | 1000 | 300 | 150 | 500 | 150 | 500 | 300 | 500 | 300 |